## Slide 1
REVISE & REJECT
M01 / STANDARD
Pole Position
Ari Dunn, Zoe King
Primary expertise: Stability
The authors study a scalar discrete-time system. They claim that the origin is asymptotically stable for every initial state. Their proof gives x[n] = 0.42ⁿ x[0], and simulated trajectories approach zero from several initial conditions. The paper makes no claim about disturbance rejection or robustness to changes in the model.
x[n+1] = 0.42 x[n]
Choose a verdict and the main rationale.
Notes: 24 fictional manuscript cards for Revise & Reject. Eight cards each are intended Accept, Revise, and Reject. Eight cards each are Guided, Standard, and Advanced. Slides alternate front and answer back. All visible content, including equations, is editable text. Duplicate a front/back pair to add a card. Keep the manuscript ID identical on both sides. Change the expertise tag or fictional author names to match your reviewer profiles. All scenarios, authors, and trial data are fictional. The intended verdict addresses the explicitly stated claim and contribution at the card level, not a complete real-world journal assessment. The PDF uses two 7 × 5 inch cards per US Letter page, with alternating front/back pages. Print at actual size, double-sided, flip on long edge. Test one sheet before a full run. Shuffle complete front/back cards before play.
Manuscript M01. Intended outcome: Accept. Accepted rationale(s): Math/Logic, Stability/Performance.
Background references for the technical principle:
https://ee363.stanford.edu/lectures/008_dtsys.pdf

## Slide 2
REVISE & REJECT
M01 / ANSWER
Pole Position
ACCEPT
ACCEPTED RATIONALE
Math/Logic / Stability/Performance
The discrete-time pole has magnitude 0.42 < 1. Therefore 0.42ⁿ approaches zero, and every trajectory approaches the origin. The proof supports the stated claim for the given model.
BASIS FOR ACCEPTANCE
The mathematical argument establishes exactly the stability property claimed. Extra robustness tests would address a different claim.
Discuss: How would the decision change if the multiplier were 1.02?
Notes: 24 fictional manuscript cards for Revise & Reject. Eight cards each are intended Accept, Revise, and Reject. Eight cards each are Guided, Standard, and Advanced. Slides alternate front and answer back. All visible content, including equations, is editable text. Duplicate a front/back pair to add a card. Keep the manuscript ID identical on both sides. Change the expertise tag or fictional author names to match your reviewer profiles. All scenarios, authors, and trial data are fictional. The intended verdict addresses the explicitly stated claim and contribution at the card level, not a complete real-world journal assessment. The PDF uses two 7 × 5 inch cards per US Letter page, with alternating front/back pages. Print at actual size, double-sided, flip on long edge. Test one sheet before a full run. Shuffle complete front/back cards before play.
M01 answer. The discrete-time pole has magnitude 0.42 < 1. Therefore 0.42ⁿ approaches zero, and every trajectory approaches the origin. The proof supports the stated claim for the given model.
Basis for acceptance: The mathematical argument establishes exactly the stability property claimed. Extra robustness tests would address a different claim.
Background references:
https://ee363.stanford.edu/lectures/008_dtsys.pdf

## Slide 3
REVISE & REJECT
M02 / STANDARD
Delay? What Delay?
Nia Volt, Hugo Moss
Primary expertise: Feedback/PID
A high-gain controller tracks a reference accurately in simulations with instantaneous measurements. The planned hardware delivers each measurement 120 ms late. The paper claims the same tracking performance on that hardware, but its analysis and simulations contain no measurement delay. Its main contribution is the controller design and the demonstrated performance in the simulated setting.
Simulation delay: 0 ms Hardware delay: 120 ms
Choose a verdict and the main rationale.
Notes: 24 fictional manuscript cards for Revise & Reject. Eight cards each are intended Accept, Revise, and Reject. Eight cards each are Guided, Standard, and Advanced. Slides alternate front and answer back. All visible content, including equations, is editable text. Duplicate a front/back pair to add a card. Keep the manuscript ID identical on both sides. Change the expertise tag or fictional author names to match your reviewer profiles. All scenarios, authors, and trial data are fictional. The intended verdict addresses the explicitly stated claim and contribution at the card level, not a complete real-world journal assessment. The PDF uses two 7 × 5 inch cards per US Letter page, with alternating front/back pages. Print at actual size, double-sided, flip on long edge. Test one sheet before a full run. Shuffle complete front/back cards before play.
Manuscript M02. Intended outcome: Revise. Accepted rationale(s): Model/Assumptions, Evidence/Validation.
This example uses a fictional scenario and a direct check of the information on the card.

## Slide 4
REVISE & REJECT
M02 / ANSWER
Delay? What Delay?
REVISE
ACCEPTED RATIONALE
Model/Assumptions / Evidence/Validation
The simulated model omits a stated feature of the hardware. The results establish performance without delay, but they do not establish unchanged performance with a 120 ms delay. This gap does not by itself prove the controller fails.
REPAIR
Include the delay in the model and evaluate it, or remove the hardware-performance claim and retain the supported simulation result.
Discuss: What evidence would support the hardware claim?
Notes: 24 fictional manuscript cards for Revise & Reject. Eight cards each are intended Accept, Revise, and Reject. Eight cards each are Guided, Standard, and Advanced. Slides alternate front and answer back. All visible content, including equations, is editable text. Duplicate a front/back pair to add a card. Keep the manuscript ID identical on both sides. Change the expertise tag or fictional author names to match your reviewer profiles. All scenarios, authors, and trial data are fictional. The intended verdict addresses the explicitly stated claim and contribution at the card level, not a complete real-world journal assessment. The PDF uses two 7 × 5 inch cards per US Letter page, with alternating front/back pages. Print at actual size, double-sided, flip on long edge. Test one sheet before a full run. Shuffle complete front/back cards before play.
M02 answer. The simulated model omits a stated feature of the hardware. The results establish performance without delay, but they do not establish unchanged performance with a 120 ms delay. This gap does not by itself prove the controller fails.
Repair: Include the delay in the model and evaluate it, or remove the hardware-performance claim and retain the supported simulation result.

## Slide 5
REVISE & REJECT
M03 / ADVANCED
Double the Gain, Double the Stability
Theo Reed, Tess Gray
Primary expertise: Stability
For the discrete-time closed loop below, the authors propose a general design rule: increasing the positive feedback gain g always improves stability. They recommend the largest gain allowed by the actuator and explicitly include g = 3 among the admissible choices. This rule is the paper's sole contribution. The argument relies only on the gain being positive.
x[n+1] = (1 − g) x[n], g > 0
Choose a verdict and the main rationale.
Notes: 24 fictional manuscript cards for Revise & Reject. Eight cards each are intended Accept, Revise, and Reject. Eight cards each are Guided, Standard, and Advanced. Slides alternate front and answer back. All visible content, including equations, is editable text. Duplicate a front/back pair to add a card. Keep the manuscript ID identical on both sides. Change the expertise tag or fictional author names to match your reviewer profiles. All scenarios, authors, and trial data are fictional. The intended verdict addresses the explicitly stated claim and contribution at the card level, not a complete real-world journal assessment. The PDF uses two 7 × 5 inch cards per US Letter page, with alternating front/back pages. Print at actual size, double-sided, flip on long edge. Test one sheet before a full run. Shuffle complete front/back cards before play.
Manuscript M03. Intended outcome: Reject. Accepted rationale(s): Math/Logic, Stability/Performance.
Background references for the technical principle:
https://ee363.stanford.edu/lectures/008_dtsys.pdf

## Slide 6
REVISE & REJECT
M03 / ANSWER
Double the Gain, Double the Stability
REJECT
ACCEPTED RATIONALE
Math/Logic / Stability/Performance
At g = 3, the pole is −2 and its magnitude exceeds one. The system is unstable for nonzero initial states. In fact, asymptotic stability requires 0 < g < 2. A direct counterexample defeats the proposed rule.
FUNDAMENTAL FLAW
Replacing the rule with a bounded gain interval changes the paper's sole contribution. More simulations cannot validate the original universal claim.
Discuss: Is g = 2 asymptotically stable? Explain.
Notes: 24 fictional manuscript cards for Revise & Reject. Eight cards each are intended Accept, Revise, and Reject. Eight cards each are Guided, Standard, and Advanced. Slides alternate front and answer back. All visible content, including equations, is editable text. Duplicate a front/back pair to add a card. Keep the manuscript ID identical on both sides. Change the expertise tag or fictional author names to match your reviewer profiles. All scenarios, authors, and trial data are fictional. The intended verdict addresses the explicitly stated claim and contribution at the card level, not a complete real-world journal assessment. The PDF uses two 7 × 5 inch cards per US Letter page, with alternating front/back pages. Print at actual size, double-sided, flip on long edge. Test one sheet before a full run. Shuffle complete front/back cards before play.
M03 answer. At g = 3, the pole is −2 and its magnitude exceeds one. The system is unstable for nonzero initial states. In fact, asymptotic stability requires 0 < g < 2. A direct counterexample defeats the proposed rule.
Fundamental flaw: Replacing the rule with a bounded gain interval changes the paper's sole contribution. More simulations cannot validate the original universal claim.
Background references:
https://ee363.stanford.edu/lectures/008_dtsys.pdf

## Slide 7
REVISE & REJECT
M04 / GUIDED
A Steady Correction
Mira Chen, Ari Dunn
Primary expertise: Feedback/PID
A tank controller increases pump flow when the measured water level is below its target and decreases pump flow when it is above. The sensor reports the level correctly, and increasing pump flow raises the level. The paper claims that this controller uses negative feedback because its corrective action opposes the measured error. It makes no claim that the closed loop must be stable for every gain.
Below target: increase flow. Above target: decrease flow.
Choose a verdict and the main rationale.
Notes: 24 fictional manuscript cards for Revise & Reject. Eight cards each are intended Accept, Revise, and Reject. Eight cards each are Guided, Standard, and Advanced. Slides alternate front and answer back. All visible content, including equations, is editable text. Duplicate a front/back pair to add a card. Keep the manuscript ID identical on both sides. Change the expertise tag or fictional author names to match your reviewer profiles. All scenarios, authors, and trial data are fictional. The intended verdict addresses the explicitly stated claim and contribution at the card level, not a complete real-world journal assessment. The PDF uses two 7 × 5 inch cards per US Letter page, with alternating front/back pages. Print at actual size, double-sided, flip on long edge. Test one sheet before a full run. Shuffle complete front/back cards before play.
Manuscript M04. Intended outcome: Accept. Accepted rationale(s): Model/Assumptions.
This example uses a fictional scenario and a direct check of the information on the card.

## Slide 8
REVISE & REJECT
M04 / ANSWER
A Steady Correction
ACCEPT
ACCEPTED RATIONALE
Model/Assumptions
The stated direction of the actuator's effect and the controller's response establish negative feedback. The authors correctly limit their claim to the feedback sign. Negative feedback alone does not guarantee stability for arbitrary gains or delays.
BASIS FOR ACCEPTANCE
The claim matches the physical model and avoids an unsupported guarantee about stability.
Discuss: What additional information would you need to assess stability?
Notes: 24 fictional manuscript cards for Revise & Reject. Eight cards each are intended Accept, Revise, and Reject. Eight cards each are Guided, Standard, and Advanced. Slides alternate front and answer back. All visible content, including equations, is editable text. Duplicate a front/back pair to add a card. Keep the manuscript ID identical on both sides. Change the expertise tag or fictional author names to match your reviewer profiles. All scenarios, authors, and trial data are fictional. The intended verdict addresses the explicitly stated claim and contribution at the card level, not a complete real-world journal assessment. The PDF uses two 7 × 5 inch cards per US Letter page, with alternating front/back pages. Print at actual size, double-sided, flip on long edge. Test one sheet before a full run. Shuffle complete front/back cards before play.
M04 answer. The stated direction of the actuator's effect and the controller's response establish negative feedback. The authors correctly limit their claim to the feedback sign. Negative feedback alone does not guarantee stability for arbitrary gains or delays.
Basis for acceptance: The claim matches the physical model and avoids an unsupported guarantee about stability.

## Slide 9
REVISE & REJECT
M05 / GUIDED
Past the Limit
Zoe King, Nia Volt
Primary expertise: Feedback/PID
A PI controller accumulates tracking error in its integral term. An unlimited-actuator simulation shows accurate tracking. The physical actuator has an input limit, but the paper never tests saturation or its effect on integral accumulation. It claims unchanged recovery from large reference changes on the device. The controller design and its demonstrated simulation performance are the main contribution.
Simulation: unlimited input. Device: bounded input.
Choose a verdict and the main rationale.
Notes: 24 fictional manuscript cards for Revise & Reject. Eight cards each are intended Accept, Revise, and Reject. Eight cards each are Guided, Standard, and Advanced. Slides alternate front and answer back. All visible content, including equations, is editable text. Duplicate a front/back pair to add a card. Keep the manuscript ID identical on both sides. Change the expertise tag or fictional author names to match your reviewer profiles. All scenarios, authors, and trial data are fictional. The intended verdict addresses the explicitly stated claim and contribution at the card level, not a complete real-world journal assessment. The PDF uses two 7 × 5 inch cards per US Letter page, with alternating front/back pages. Print at actual size, double-sided, flip on long edge. Test one sheet before a full run. Shuffle complete front/back cards before play.
Manuscript M05. Intended outcome: Revise. Accepted rationale(s): Model/Assumptions, Evidence/Validation.
This example uses a fictional scenario and a direct check of the information on the card.

## Slide 10
REVISE & REJECT
M05 / ANSWER
Past the Limit
REVISE
ACCEPTED RATIONALE
Model/Assumptions / Evidence/Validation
Actuator saturation changes the implemented loop, and accumulated integral error can affect recovery. The unlimited-actuator experiment does not support the device claim. The card does not establish that this controller necessarily fails.
REPAIR
Test the input limit and address integral accumulation if necessary, or restrict the claim to the simulated unlimited-actuator setting.
Discuss: Why might the integral term keep growing while the actuator is at its limit?
Notes: 24 fictional manuscript cards for Revise & Reject. Eight cards each are intended Accept, Revise, and Reject. Eight cards each are Guided, Standard, and Advanced. Slides alternate front and answer back. All visible content, including equations, is editable text. Duplicate a front/back pair to add a card. Keep the manuscript ID identical on both sides. Change the expertise tag or fictional author names to match your reviewer profiles. All scenarios, authors, and trial data are fictional. The intended verdict addresses the explicitly stated claim and contribution at the card level, not a complete real-world journal assessment. The PDF uses two 7 × 5 inch cards per US Letter page, with alternating front/back pages. Print at actual size, double-sided, flip on long edge. Test one sheet before a full run. Shuffle complete front/back cards before play.
M05 answer. Actuator saturation changes the implemented loop, and accumulated integral error can affect recovery. The unlimited-actuator experiment does not support the device claim. The card does not establish that this controller necessarily fails.
Repair: Test the input limit and address integral accumulation if necessary, or restrict the claim to the simulated unlimited-actuator setting.

## Slide 11
REVISE & REJECT
M06 / GUIDED
Response Under Load
Hugo Moss, Theo Reed
Primary expertise: Feedback/PID
A pump controls the scalar plant below. Its actuator always satisfies |u| ≤ 1. The authors claim that their new controller makes x approach every constant target, including target r = 2. Their sole contribution is this unrestricted tracking guarantee. At a constant tracked target, the plant equation requires the steady input to equal the target. No other actuator or external input is present.
dx/dt = −x + u, |u| ≤ 1, target r = 2
Choose a verdict and the main rationale.
Notes: 24 fictional manuscript cards for Revise & Reject. Eight cards each are intended Accept, Revise, and Reject. Eight cards each are Guided, Standard, and Advanced. Slides alternate front and answer back. All visible content, including equations, is editable text. Duplicate a front/back pair to add a card. Keep the manuscript ID identical on both sides. Change the expertise tag or fictional author names to match your reviewer profiles. All scenarios, authors, and trial data are fictional. The intended verdict addresses the explicitly stated claim and contribution at the card level, not a complete real-world journal assessment. The PDF uses two 7 × 5 inch cards per US Letter page, with alternating front/back pages. Print at actual size, double-sided, flip on long edge. Test one sheet before a full run. Shuffle complete front/back cards before play.
Manuscript M06. Intended outcome: Reject. Accepted rationale(s): Model/Assumptions, Stability/Performance.
This example uses a fictional scenario and a direct check of the information on the card.

## Slide 12
REVISE & REJECT
M06 / ANSWER
Response Under Load
REJECT
ACCEPTED RATIONALE
Model/Assumptions / Stability/Performance
Holding x = 2 requires u = 2, which the actuator cannot produce. More generally, from x(0) = 0 and u ≤ 1, the state cannot approach 2. The guarantee contradicts a physical constraint explicitly included in the model.
FUNDAMENTAL FLAW
The sole guarantee is impossible under the given actuator limit. Restricting targets or changing the actuator materially replaces that contribution.
Discuss: Which constant targets can satisfy the equilibrium input constraint?
Notes: 24 fictional manuscript cards for Revise & Reject. Eight cards each are intended Accept, Revise, and Reject. Eight cards each are Guided, Standard, and Advanced. Slides alternate front and answer back. All visible content, including equations, is editable text. Duplicate a front/back pair to add a card. Keep the manuscript ID identical on both sides. Change the expertise tag or fictional author names to match your reviewer profiles. All scenarios, authors, and trial data are fictional. The intended verdict addresses the explicitly stated claim and contribution at the card level, not a complete real-world journal assessment. The PDF uses two 7 × 5 inch cards per US Letter page, with alternating front/back pages. Print at actual size, double-sided, flip on long edge. Test one sheet before a full run. Shuffle complete front/back cards before play.
M06 answer. Holding x = 2 requires u = 2, which the actuator cannot produce. More generally, from x(0) = 0 and u ≤ 1, the state cannot approach 2. The guarantee contradicts a physical constraint explicitly included in the model.
Fundamental flaw: The sole guarantee is impossible under the given actuator limit. Restricting targets or changing the actuator materially replaces that contribution.

## Slide 13
REVISE & REJECT
M07 / ADVANCED
Feedback on Paper
Tess Gray, Mira Chen
Primary expertise: Linear Systems
The paper claims that state feedback u = −Kx can stabilize the origin of the continuous-time system below for every initial state. The authors describe both states as controllable because both appear in A. The only input acts on the first state. The paper's sole result is a guarantee of global asymptotic stabilization of this two-state plant by choosing K.
A = [[−1, 0], [0, 1]], B = [1, 0]ᵀ
Choose a verdict and the main rationale.
Notes: 24 fictional manuscript cards for Revise & Reject. Eight cards each are intended Accept, Revise, and Reject. Eight cards each are Guided, Standard, and Advanced. Slides alternate front and answer back. All visible content, including equations, is editable text. Duplicate a front/back pair to add a card. Keep the manuscript ID identical on both sides. Change the expertise tag or fictional author names to match your reviewer profiles. All scenarios, authors, and trial data are fictional. The intended verdict addresses the explicitly stated claim and contribution at the card level, not a complete real-world journal assessment. The PDF uses two 7 × 5 inch cards per US Letter page, with alternating front/back pages. Print at actual size, double-sided, flip on long edge. Test one sheet before a full run. Shuffle complete front/back cards before play.
Manuscript M07. Intended outcome: Reject. Accepted rationale(s): Math/Logic, Stability/Performance.
Background references for the technical principle:
https://underactuated.mit.edu/acrobot.html

## Slide 14
REVISE & REJECT
M07 / ANSWER
Feedback on Paper
REJECT
ACCEPTED RATIONALE
Math/Logic / Stability/Performance
The second state obeys dx₂/dt = x₂ regardless of the feedback gain. Thus x₂(t) = exp(t)x₂(0), and any nonzero initial second state diverges. The unstable mode is uncontrollable, so state feedback cannot stabilize the full system.
FUNDAMENTAL FLAW
The proposed guarantee is impossible for the stated plant. An extra actuator or a different plant would change the problem and the central result.
Discuss: Would an uncontrollable but stable second mode create the same obstacle?
Notes: 24 fictional manuscript cards for Revise & Reject. Eight cards each are intended Accept, Revise, and Reject. Eight cards each are Guided, Standard, and Advanced. Slides alternate front and answer back. All visible content, including equations, is editable text. Duplicate a front/back pair to add a card. Keep the manuscript ID identical on both sides. Change the expertise tag or fictional author names to match your reviewer profiles. All scenarios, authors, and trial data are fictional. The intended verdict addresses the explicitly stated claim and contribution at the card level, not a complete real-world journal assessment. The PDF uses two 7 × 5 inch cards per US Letter page, with alternating front/back pages. Print at actual size, double-sided, flip on long edge. Test one sheet before a full run. Shuffle complete front/back cards before play.
M07 answer. The second state obeys dx₂/dt = x₂ regardless of the feedback gain. Thus x₂(t) = exp(t)x₂(0), and any nonzero initial second state diverges. The unstable mode is uncontrollable, so state feedback cannot stabilize the full system.
Fundamental flaw: The proposed guarantee is impossible for the stated plant. An extra actuator or a different plant would change the problem and the central result.
Background references:
https://underactuated.mit.edu/acrobot.html

## Slide 15
REVISE & REJECT
M08 / ADVANCED
Looking Inside
Ari Dunn, Hugo Moss
Primary expertise: Estimation
A paper studies the noiseless discrete-time system x[n+1] = Ax[n] and y[n] = Cx[n], with the matrices below. It claims that two consecutive output samples determine the two components of x[0] uniquely. The derivation gives y[0] = x₁[0] and y[1] = x₁[0] + x₂[0]. It limits the claim to this exact known model without process or measurement noise.
A = [[1, 1], [0, 1]], C = [1, 0]
Choose a verdict and the main rationale.
Notes: 24 fictional manuscript cards for Revise & Reject. Eight cards each are intended Accept, Revise, and Reject. Eight cards each are Guided, Standard, and Advanced. Slides alternate front and answer back. All visible content, including equations, is editable text. Duplicate a front/back pair to add a card. Keep the manuscript ID identical on both sides. Change the expertise tag or fictional author names to match your reviewer profiles. All scenarios, authors, and trial data are fictional. The intended verdict addresses the explicitly stated claim and contribution at the card level, not a complete real-world journal assessment. The PDF uses two 7 × 5 inch cards per US Letter page, with alternating front/back pages. Print at actual size, double-sided, flip on long edge. Test one sheet before a full run. Shuffle complete front/back cards before play.
Manuscript M08. Intended outcome: Accept. Accepted rationale(s): Math/Logic.
Background references for the technical principle:
https://ee363.stanford.edu/lectures/011_observ.pdf

## Slide 16
REVISE & REJECT
M08 / ANSWER
Looking Inside
ACCEPT
ACCEPTED RATIONALE
Math/Logic
The observability matrix has rows C and CA: [[1, 0], [1, 1]]. Its determinant is one, so it has full rank. Equivalently, x₁[0] = y[0] and x₂[0] = y[1] − y[0]. The reconstruction claim is correct.
BASIS FOR ACCEPTANCE
The argument proves unique state reconstruction under the explicitly stated noiseless assumptions.
Discuss: What changes if C = [0, 1]?
Notes: 24 fictional manuscript cards for Revise & Reject. Eight cards each are intended Accept, Revise, and Reject. Eight cards each are Guided, Standard, and Advanced. Slides alternate front and answer back. All visible content, including equations, is editable text. Duplicate a front/back pair to add a card. Keep the manuscript ID identical on both sides. Change the expertise tag or fictional author names to match your reviewer profiles. All scenarios, authors, and trial data are fictional. The intended verdict addresses the explicitly stated claim and contribution at the card level, not a complete real-world journal assessment. The PDF uses two 7 × 5 inch cards per US Letter page, with alternating front/back pages. Print at actual size, double-sided, flip on long edge. Test one sheet before a full run. Shuffle complete front/back cards before play.
M08 answer. The observability matrix has rows C and CA: [[1, 0], [1, 1]]. Its determinant is one, so it has full rank. Equivalently, x₁[0] = y[0] and x₂[0] = y[1] − y[0]. The reconstruction claim is correct.
Basis for acceptance: The argument proves unique state reconstruction under the explicitly stated noiseless assumptions.
Background references:
https://ee363.stanford.edu/lectures/011_observ.pdf

## Slide 17
REVISE & REJECT
M09 / STANDARD
Shared Noise
Nia Volt, Tess Gray
Primary expertise: Estimation
Two sensors measure one scalar state. Their noises have mean zero, variance 1, and simultaneous covariance 0.8. A Kalman filter uses R = I instead. The paper reports accurate state estimates and claims calibrated uncertainty for these sensors. Its main contribution is the estimation pipeline, which already supports a general measurement covariance matrix. The paper never evaluates the stated correlation.
Actual R = [[1, 0.8], [0.8, 1]] Used R = I
Choose a verdict and the main rationale.
Notes: 24 fictional manuscript cards for Revise & Reject. Eight cards each are intended Accept, Revise, and Reject. Eight cards each are Guided, Standard, and Advanced. Slides alternate front and answer back. All visible content, including equations, is editable text. Duplicate a front/back pair to add a card. Keep the manuscript ID identical on both sides. Change the expertise tag or fictional author names to match your reviewer profiles. All scenarios, authors, and trial data are fictional. The intended verdict addresses the explicitly stated claim and contribution at the card level, not a complete real-world journal assessment. The PDF uses two 7 × 5 inch cards per US Letter page, with alternating front/back pages. Print at actual size, double-sided, flip on long edge. Test one sheet before a full run. Shuffle complete front/back cards before play.
Manuscript M09. Intended outcome: Revise. Accepted rationale(s): Model/Assumptions, Evidence/Validation.
Background references for the technical principle:
https://ee363.stanford.edu/lectures/021_kf.pdf

## Slide 18
REVISE & REJECT
M09 / ANSWER
Shared Noise
REVISE
ACCEPTED RATIONALE
Model/Assumptions / Evidence/Validation
The implemented noise model ignores a stated correlation. Good point estimates alone do not establish calibrated uncertainty. Using the actual covariance can preserve the estimation pipeline while addressing the mismatch.
REPAIR
Use the measured full covariance and reassess uncertainty calibration on the trials. Update any performance claims that change.
Discuss: Why can similar point estimates have different uncertainty estimates?
Notes: 24 fictional manuscript cards for Revise & Reject. Eight cards each are intended Accept, Revise, and Reject. Eight cards each are Guided, Standard, and Advanced. Slides alternate front and answer back. All visible content, including equations, is editable text. Duplicate a front/back pair to add a card. Keep the manuscript ID identical on both sides. Change the expertise tag or fictional author names to match your reviewer profiles. All scenarios, authors, and trial data are fictional. The intended verdict addresses the explicitly stated claim and contribution at the card level, not a complete real-world journal assessment. The PDF uses two 7 × 5 inch cards per US Letter page, with alternating front/back pages. Print at actual size, double-sided, flip on long edge. Test one sheet before a full run. Shuffle complete front/back cards before play.
M09 answer. The implemented noise model ignores a stated correlation. Good point estimates alone do not establish calibrated uncertainty. Using the actual covariance can preserve the estimation pipeline while addressing the mismatch.
Repair: Use the measured full covariance and reassess uncertainty calibration on the trials. Update any performance claims that change.
Background references:
https://ee363.stanford.edu/lectures/021_kf.pdf

## Slide 19
REVISE & REJECT
M10 / STANDARD
Two Sensors, One Signal
Theo Reed, Zoe King
Primary expertise: Estimation
A device copies one sensor reading into two channels. Both channels contain exactly the same zero-mean noise v with variance 1. The paper averages the two channels and claims that this duplication alone halves the estimation-error variance, creating independent information at no sensor cost. That variance reduction is the sole contribution. The true state x is fixed during the reading.
y₁ = x + v, y₂ = x + v, x̂ = (y₁ + y₂)/2
Choose a verdict and the main rationale.
Notes: 24 fictional manuscript cards for Revise & Reject. Eight cards each are intended Accept, Revise, and Reject. Eight cards each are Guided, Standard, and Advanced. Slides alternate front and answer back. All visible content, including equations, is editable text. Duplicate a front/back pair to add a card. Keep the manuscript ID identical on both sides. Change the expertise tag or fictional author names to match your reviewer profiles. All scenarios, authors, and trial data are fictional. The intended verdict addresses the explicitly stated claim and contribution at the card level, not a complete real-world journal assessment. The PDF uses two 7 × 5 inch cards per US Letter page, with alternating front/back pages. Print at actual size, double-sided, flip on long edge. Test one sheet before a full run. Shuffle complete front/back cards before play.
Manuscript M10. Intended outcome: Reject. Accepted rationale(s): Math/Logic, Model/Assumptions.
This example uses a fictional scenario and a direct check of the information on the card.

## Slide 20
REVISE & REJECT
M10 / ANSWER
Two Sensors, One Signal
REJECT
ACCEPTED RATIONALE
Math/Logic / Model/Assumptions
The average remains x + v, so its error variance is still 1. Copying a measurement does not create independent noise realizations. A variance of 1/2 would require two independent measurements with equal variance, which this setup lacks.
FUNDAMENTAL FLAW
The sole claimed improvement disappears when the stated dependence is included. Adding an independent sensor would change the proposed method.
Discuss: What is the variance of the average if the channel noises are independent?
Notes: 24 fictional manuscript cards for Revise & Reject. Eight cards each are intended Accept, Revise, and Reject. Eight cards each are Guided, Standard, and Advanced. Slides alternate front and answer back. All visible content, including equations, is editable text. Duplicate a front/back pair to add a card. Keep the manuscript ID identical on both sides. Change the expertise tag or fictional author names to match your reviewer profiles. All scenarios, authors, and trial data are fictional. The intended verdict addresses the explicitly stated claim and contribution at the card level, not a complete real-world journal assessment. The PDF uses two 7 × 5 inch cards per US Letter page, with alternating front/back pages. Print at actual size, double-sided, flip on long edge. Test one sheet before a full run. Shuffle complete front/back cards before play.
M10 answer. The average remains x + v, so its error variance is still 1. Copying a measurement does not create independent noise realizations. A variance of 1/2 would require two independent measurements with equal variance, which this setup lacks.
Fundamental flaw: The sole claimed improvement disappears when the stated dependence is included. Adding an independent sensor would change the proposed method.

## Slide 21
REVISE & REJECT
M11 / GUIDED
Different Starts
Mira Chen, Nia Volt
Primary expertise: Multi-agent Systems
Two agents continuously exchange their scalar values without delay. Each moves its value toward the other's value at the same rate. Their initial values are 2 and 6. The paper shows that their difference decays to zero and their sum stays equal to 8. It claims that both agents approach the initial average, 4, under these stated communication conditions.
dx₁/dt = x₂ − x₁ dx₂/dt = x₁ − x₂
Choose a verdict and the main rationale.
Notes: 24 fictional manuscript cards for Revise & Reject. Eight cards each are intended Accept, Revise, and Reject. Eight cards each are Guided, Standard, and Advanced. Slides alternate front and answer back. All visible content, including equations, is editable text. Duplicate a front/back pair to add a card. Keep the manuscript ID identical on both sides. Change the expertise tag or fictional author names to match your reviewer profiles. All scenarios, authors, and trial data are fictional. The intended verdict addresses the explicitly stated claim and contribution at the card level, not a complete real-world journal assessment. The PDF uses two 7 × 5 inch cards per US Letter page, with alternating front/back pages. Print at actual size, double-sided, flip on long edge. Test one sheet before a full run. Shuffle complete front/back cards before play.
Manuscript M11. Intended outcome: Accept. Accepted rationale(s): Math/Logic, Stability/Performance.
This example uses a fictional scenario and a direct check of the information on the card.

## Slide 22
REVISE & REJECT
M11 / ANSWER
Different Starts
ACCEPT
ACCEPTED RATIONALE
Math/Logic / Stability/Performance
Adding the equations gives a constant sum. Subtracting them gives d(x₁ − x₂)/dt = −2(x₁ − x₂), so the difference approaches zero. Equal limiting values with sum 8 must both equal 4.
BASIS FOR ACCEPTANCE
The argument establishes both agreement and preservation of the average for the stated two-agent model.
Discuss: Would agreement alone prove convergence to the initial average?
Notes: 24 fictional manuscript cards for Revise & Reject. Eight cards each are intended Accept, Revise, and Reject. Eight cards each are Guided, Standard, and Advanced. Slides alternate front and answer back. All visible content, including equations, is editable text. Duplicate a front/back pair to add a card. Keep the manuscript ID identical on both sides. Change the expertise tag or fictional author names to match your reviewer profiles. All scenarios, authors, and trial data are fictional. The intended verdict addresses the explicitly stated claim and contribution at the card level, not a complete real-world journal assessment. The PDF uses two 7 × 5 inch cards per US Letter page, with alternating front/back pages. Print at actual size, double-sided, flip on long edge. Test one sheet before a full run. Shuffle complete front/back cards before play.
M11 answer. Adding the equations gives a constant sum. Subtracting them gives d(x₁ − x₂)/dt = −2(x₁ − x₂), so the difference approaches zero. Equal limiting values with sum 8 must both equal 4.
Basis for acceptance: The argument establishes both agreement and preservation of the average for the stated two-agent model.

## Slide 23
REVISE & REJECT
M12 / STANDARD
Local Agreement
Hugo Moss, Mira Chen
Primary expertise: Multi-agent Systems
Four agents use continuous-time consensus with equal bidirectional weights. Agents 1 and 2 communicate only with each other, as do agents 3 and 4. Initial values are (0, 2, 8, 10). Simulations show agreement within each pair. The contribution studies coordination within separate groups, but the conclusion claims that all four agents converge to one common value.
Links: 1—2 and 3—4 only. Initial values: (0, 2, 8, 10)
Choose a verdict and the main rationale.
Notes: 24 fictional manuscript cards for Revise & Reject. Eight cards each are intended Accept, Revise, and Reject. Eight cards each are Guided, Standard, and Advanced. Slides alternate front and answer back. All visible content, including equations, is editable text. Duplicate a front/back pair to add a card. Keep the manuscript ID identical on both sides. Change the expertise tag or fictional author names to match your reviewer profiles. All scenarios, authors, and trial data are fictional. The intended verdict addresses the explicitly stated claim and contribution at the card level, not a complete real-world journal assessment. The PDF uses two 7 × 5 inch cards per US Letter page, with alternating front/back pages. Print at actual size, double-sided, flip on long edge. Test one sheet before a full run. Shuffle complete front/back cards before play.
Manuscript M12. Intended outcome: Revise. Accepted rationale(s): Model/Assumptions, Stability/Performance.
This example uses a fictional scenario and a direct check of the information on the card.

## Slide 24
REVISE & REJECT
M12 / ANSWER
Local Agreement
REVISE
ACCEPTED RATIONALE
Model/Assumptions / Stability/Performance
The disconnected pairs converge separately to 1 and 9. The results support agreement within each group, which is the stated study's contribution. They do not support one value shared by all four agents.
REPAIR
Limit the conclusion to consensus within connected groups and state the connectivity assumption needed for a team-wide result.
Discuss: What role would a communication link between the groups play?
Notes: 24 fictional manuscript cards for Revise & Reject. Eight cards each are intended Accept, Revise, and Reject. Eight cards each are Guided, Standard, and Advanced. Slides alternate front and answer back. All visible content, including equations, is editable text. Duplicate a front/back pair to add a card. Keep the manuscript ID identical on both sides. Change the expertise tag or fictional author names to match your reviewer profiles. All scenarios, authors, and trial data are fictional. The intended verdict addresses the explicitly stated claim and contribution at the card level, not a complete real-world journal assessment. The PDF uses two 7 × 5 inch cards per US Letter page, with alternating front/back pages. Print at actual size, double-sided, flip on long edge. Test one sheet before a full run. Shuffle complete front/back cards before play.
M12 answer. The disconnected pairs converge separately to 1 and 9. The results support agreement within each group, which is the stated study's contribution. They do not support one value shared by all four agents.
Repair: Limit the conclusion to consensus within connected groups and state the connectivity assumption needed for a team-wide result.

## Slide 25
REVISE & REJECT
M13 / ADVANCED
One Step Together
Tess Gray, Ari Dunn
Primary expertise: Multi-agent Systems
A paper proposes the discrete-time update x[n+1] = Wx[n] below. It claims that row sums equal to one guarantee convergence to the arithmetic mean of the initial states. Preserving that mean for every initial state is the method's sole claimed advance. For initial values (0, 3), the authors cite agreement between the agents as sufficient evidence of average consensus.
W = [[0.5, 0.5], [1, 0]], x[0] = [0, 3]ᵀ
Choose a verdict and the main rationale.
Notes: 24 fictional manuscript cards for Revise & Reject. Eight cards each are intended Accept, Revise, and Reject. Eight cards each are Guided, Standard, and Advanced. Slides alternate front and answer back. All visible content, including equations, is editable text. Duplicate a front/back pair to add a card. Keep the manuscript ID identical on both sides. Change the expertise tag or fictional author names to match your reviewer profiles. All scenarios, authors, and trial data are fictional. The intended verdict addresses the explicitly stated claim and contribution at the card level, not a complete real-world journal assessment. The PDF uses two 7 × 5 inch cards per US Letter page, with alternating front/back pages. Print at actual size, double-sided, flip on long edge. Test one sheet before a full run. Shuffle complete front/back cards before play.
Manuscript M13. Intended outcome: Reject. Accepted rationale(s): Math/Logic, Stability/Performance.
This example uses a fictional scenario and a direct check of the information on the card.

## Slide 26
REVISE & REJECT
M13 / ANSWER
One Step Together
REJECT
ACCEPTED RATIONALE
Math/Logic / Stability/Performance
This W converges to consensus at a weighted mean: (2/3)x₁[0] + (1/3)x₂[0] = 1. The arithmetic mean is 1.5. Row sums of one do not preserve the sum of states. Here the column sums are 1.5 and 0.5.
FUNDAMENTAL FLAW
The claimed average-preservation property fails for the explicit example. A different update matrix or a weighted-mean claim replaces the sole contribution.
Discuss: Which matrix condition would preserve the sum at each step?
Notes: 24 fictional manuscript cards for Revise & Reject. Eight cards each are intended Accept, Revise, and Reject. Eight cards each are Guided, Standard, and Advanced. Slides alternate front and answer back. All visible content, including equations, is editable text. Duplicate a front/back pair to add a card. Keep the manuscript ID identical on both sides. Change the expertise tag or fictional author names to match your reviewer profiles. All scenarios, authors, and trial data are fictional. The intended verdict addresses the explicitly stated claim and contribution at the card level, not a complete real-world journal assessment. The PDF uses two 7 × 5 inch cards per US Letter page, with alternating front/back pages. Print at actual size, double-sided, flip on long edge. Test one sheet before a full run. Shuffle complete front/back cards before play.
M13 answer. This W converges to consensus at a weighted mean: (2/3)x₁[0] + (1/3)x₂[0] = 1. The arithmetic mean is 1.5. Row sums of one do not preserve the sum of states. Here the column sums are 1.5 and 0.5.
Fundamental flaw: The claimed average-preservation property fails for the explicit example. A different update matrix or a weighted-mean claim replaces the sole contribution.

## Slide 27
REVISE & REJECT
M14 / STANDARD
Smooth on Screen
Zoe King, Hugo Moss
Primary expertise: Feedback/PID
A tuning procedure produces tracking RMSE 0.8 in one noisy simulation, versus 1.0 for a baseline. Both use the same plant and initial condition but different noise realizations. The paper claims lower expected RMSE in general. Its contribution includes a fully specified tuning algorithm. It reports no repeated trials or uncertainty estimates.
One run each: proposed RMSE 0.8 baseline RMSE 1.0
Choose a verdict and the main rationale.
Notes: 24 fictional manuscript cards for Revise & Reject. Eight cards each are intended Accept, Revise, and Reject. Eight cards each are Guided, Standard, and Advanced. Slides alternate front and answer back. All visible content, including equations, is editable text. Duplicate a front/back pair to add a card. Keep the manuscript ID identical on both sides. Change the expertise tag or fictional author names to match your reviewer profiles. All scenarios, authors, and trial data are fictional. The intended verdict addresses the explicitly stated claim and contribution at the card level, not a complete real-world journal assessment. The PDF uses two 7 × 5 inch cards per US Letter page, with alternating front/back pages. Print at actual size, double-sided, flip on long edge. Test one sheet before a full run. Shuffle complete front/back cards before play.
Manuscript M14. Intended outcome: Revise. Accepted rationale(s): Evidence/Validation.
This example uses a fictional scenario and a direct check of the information on the card.

## Slide 28
REVISE & REJECT
M14 / ANSWER
Smooth on Screen
REVISE
ACCEPTED RATIONALE
Evidence/Validation
One noisy run per controller cannot establish a general reduction in expected error, especially with different noise realizations. The algorithm remains a usable contribution, and the comparative claim can be evaluated with an appropriate experiment.
REPAIR
Run repeated paired comparisons with common conditions and noise realizations, report variability, and align the conclusion with the resulting evidence.
Discuss: Why are matched noise realizations useful in a comparison?
Notes: 24 fictional manuscript cards for Revise & Reject. Eight cards each are intended Accept, Revise, and Reject. Eight cards each are Guided, Standard, and Advanced. Slides alternate front and answer back. All visible content, including equations, is editable text. Duplicate a front/back pair to add a card. Keep the manuscript ID identical on both sides. Change the expertise tag or fictional author names to match your reviewer profiles. All scenarios, authors, and trial data are fictional. The intended verdict addresses the explicitly stated claim and contribution at the card level, not a complete real-world journal assessment. The PDF uses two 7 × 5 inch cards per US Letter page, with alternating front/back pages. Print at actual size, double-sided, flip on long edge. Test one sheet before a full run. Shuffle complete front/back cards before play.
M14 answer. One noisy run per controller cannot establish a general reduction in expected error, especially with different noise realizations. The algorithm remains a usable contribution, and the comparative claim can be evaluated with an appropriate experiment.
Repair: Run repeated paired comparisons with common conditions and noise realizations, report variability, and align the conclusion with the resulting evidence.

## Slide 29
REVISE & REJECT
M15 / GUIDED
A Fair Trial
Ari Dunn, Nia Volt
Primary expertise: Feedback/PID
Two controllers complete all 30 trials on the same specified set of test conditions. Each paired trial uses the same starting state and disturbance for both controllers. The paper provides every settling time and reports medians of 20 s for the proposed controller and 24 s for the baseline. It claims only a lower median settling time on this test set and explicitly leaves other plants and conditions untested.
30 trials each. Median settling time: 20 s versus 24 s.
Choose a verdict and the main rationale.
Notes: 24 fictional manuscript cards for Revise & Reject. Eight cards each are intended Accept, Revise, and Reject. Eight cards each are Guided, Standard, and Advanced. Slides alternate front and answer back. All visible content, including equations, is editable text. Duplicate a front/back pair to add a card. Keep the manuscript ID identical on both sides. Change the expertise tag or fictional author names to match your reviewer profiles. All scenarios, authors, and trial data are fictional. The intended verdict addresses the explicitly stated claim and contribution at the card level, not a complete real-world journal assessment. The PDF uses two 7 × 5 inch cards per US Letter page, with alternating front/back pages. Print at actual size, double-sided, flip on long edge. Test one sheet before a full run. Shuffle complete front/back cards before play.
Manuscript M15. Intended outcome: Accept. Accepted rationale(s): Evidence/Validation.
This example uses a fictional scenario and a direct check of the information on the card.

## Slide 30
REVISE & REJECT
M15 / ANSWER
A Fair Trial
ACCEPT
ACCEPTED RATIONALE
Evidence/Validation
The complete paired data and reported medians support the limited descriptive claim about this test set. The paper does not turn that observed comparison into an unsupported universal guarantee or a claim about population means.
BASIS FOR ACCEPTANCE
The evidence matches the comparison and the conclusion stays within the evaluated conditions.
Discuss: What additional evidence would support a claim about other plants?
Notes: 24 fictional manuscript cards for Revise & Reject. Eight cards each are intended Accept, Revise, and Reject. Eight cards each are Guided, Standard, and Advanced. Slides alternate front and answer back. All visible content, including equations, is editable text. Duplicate a front/back pair to add a card. Keep the manuscript ID identical on both sides. Change the expertise tag or fictional author names to match your reviewer profiles. All scenarios, authors, and trial data are fictional. The intended verdict addresses the explicitly stated claim and contribution at the card level, not a complete real-world journal assessment. The PDF uses two 7 × 5 inch cards per US Letter page, with alternating front/back pages. Print at actual size, double-sided, flip on long edge. Test one sheet before a full run. Shuffle complete front/back cards before play.
M15 answer. The complete paired data and reported medians support the limited descriptive claim about this test set. The paper does not turn that observed comparison into an unsupported universal guarantee or a claim about population means.
Basis for acceptance: The evidence matches the comparison and the conclusion stays within the evaluated conditions.

## Slide 31
REVISE & REJECT
M16 / GUIDED
Timing the Trials
Theo Reed, Hugo Moss
Primary expertise: Feedback/PID
Two controllers face the same ten tests with a 60 s timeout. The proposed controller finishes twice in 8 s and times out eight times. The baseline finishes every test in 12 s. After discarding timeouts, the paper claims greater reliability and faster completion across the full benchmark. This joint superiority claim is its sole contribution.
Proposed: 2/10 successes. Baseline: 10/10 successes.
Choose a verdict and the main rationale.
Notes: 24 fictional manuscript cards for Revise & Reject. Eight cards each are intended Accept, Revise, and Reject. Eight cards each are Guided, Standard, and Advanced. Slides alternate front and answer back. All visible content, including equations, is editable text. Duplicate a front/back pair to add a card. Keep the manuscript ID identical on both sides. Change the expertise tag or fictional author names to match your reviewer profiles. All scenarios, authors, and trial data are fictional. The intended verdict addresses the explicitly stated claim and contribution at the card level, not a complete real-world journal assessment. The PDF uses two 7 × 5 inch cards per US Letter page, with alternating front/back pages. Print at actual size, double-sided, flip on long edge. Test one sheet before a full run. Shuffle complete front/back cards before play.
Manuscript M16. Intended outcome: Reject. Accepted rationale(s): Evidence/Validation.
This example uses a fictional scenario and a direct check of the information on the card.

## Slide 32
REVISE & REJECT
M16 / ANSWER
Timing the Trials
REJECT
ACCEPTED RATIONALE
Evidence/Validation
The stated success rates directly contradict the reliability claim. Comparing times only after discarding eight failures also fails to establish speed across the full benchmark. The problem is contradicted evidence, rather than merely an absent experiment.
FUNDAMENTAL FLAW
An honest report removes the paper's sole joint-superiority result. Extra wording cannot make the existing success counts support that claim.
Discuss: How should a benchmark report both completion times and failures?
Notes: 24 fictional manuscript cards for Revise & Reject. Eight cards each are intended Accept, Revise, and Reject. Eight cards each are Guided, Standard, and Advanced. Slides alternate front and answer back. All visible content, including equations, is editable text. Duplicate a front/back pair to add a card. Keep the manuscript ID identical on both sides. Change the expertise tag or fictional author names to match your reviewer profiles. All scenarios, authors, and trial data are fictional. The intended verdict addresses the explicitly stated claim and contribution at the card level, not a complete real-world journal assessment. The PDF uses two 7 × 5 inch cards per US Letter page, with alternating front/back pages. Print at actual size, double-sided, flip on long edge. Test one sheet before a full run. Shuffle complete front/back cards before play.
M16 answer. The stated success rates directly contradict the reliability claim. Comparing times only after discarding eight failures also fails to establish speed across the full benchmark. The problem is contradicted evidence, rather than merely an absent experiment.
Fundamental flaw: An honest report removes the paper's sole joint-superiority result. Extra wording cannot make the existing success counts support that claim.

## Slide 33
REVISE & REJECT
M17 / GUIDED
A Recipe to Repeat
Mira Chen, Zoe King
Primary expertise: Linear Systems
A teaching paper gives a complete scalar simulation recipe. Set x[0] = 8 and u[n] = −0.5x[n]. At each step compute x[n+1] = x[n] + u[n], using the current state. Use exact arithmetic with no noise. The authors report x[1] = 4, x[2] = 2, and x[3] = 1, and claim that readers can reproduce these values from the supplied instructions.
x[0] = 8 u[n] = −0.5x[n] x[n+1] = x[n] + u[n]
Choose a verdict and the main rationale.
Notes: 24 fictional manuscript cards for Revise & Reject. Eight cards each are intended Accept, Revise, and Reject. Eight cards each are Guided, Standard, and Advanced. Slides alternate front and answer back. All visible content, including equations, is editable text. Duplicate a front/back pair to add a card. Keep the manuscript ID identical on both sides. Change the expertise tag or fictional author names to match your reviewer profiles. All scenarios, authors, and trial data are fictional. The intended verdict addresses the explicitly stated claim and contribution at the card level, not a complete real-world journal assessment. The PDF uses two 7 × 5 inch cards per US Letter page, with alternating front/back pages. Print at actual size, double-sided, flip on long edge. Test one sheet before a full run. Shuffle complete front/back cards before play.
Manuscript M17. Intended outcome: Accept. Accepted rationale(s): Clarity/Reproducibility, Math/Logic.
This example uses a fictional scenario and a direct check of the information on the card.

## Slide 34
REVISE & REJECT
M17 / ANSWER
A Recipe to Repeat
ACCEPT
ACCEPTED RATIONALE
Clarity/Reproducibility / Math/Logic
Substituting the controller gives x[n+1] = 0.5x[n], which produces the reported sequence. The initial state, update order, noise assumption, and arithmetic convention specify the requested computation completely.
BASIS FOR ACCEPTANCE
The reproducibility claim is specific and the card includes the information needed to check it.
Discuss: Which supplied details prevent two readers from simulating different systems?
Notes: 24 fictional manuscript cards for Revise & Reject. Eight cards each are intended Accept, Revise, and Reject. Eight cards each are Guided, Standard, and Advanced. Slides alternate front and answer back. All visible content, including equations, is editable text. Duplicate a front/back pair to add a card. Keep the manuscript ID identical on both sides. Change the expertise tag or fictional author names to match your reviewer profiles. All scenarios, authors, and trial data are fictional. The intended verdict addresses the explicitly stated claim and contribution at the card level, not a complete real-world journal assessment. The PDF uses two 7 × 5 inch cards per US Letter page, with alternating front/back pages. Print at actual size, double-sided, flip on long edge. Test one sheet before a full run. Shuffle complete front/back cards before play.
M17 answer. Substituting the controller gives x[n+1] = 0.5x[n], which produces the reported sequence. The initial state, update order, noise assumption, and arithmetic convention specify the requested computation completely.
Basis for acceptance: The reproducibility claim is specific and the card includes the information needed to check it.

## Slide 35
REVISE & REJECT
M18 / STANDARD
The Missing Clock
Nia Volt, Mira Chen
Primary expertise: Feedback/PID
A digital PI-controller study provides the plant, gains, initial conditions, input limits, and complete reference signal. Its implementation updates the integral state with the equation below. The sample period T is missing from both the text and code listing. The paper claims that readers can reproduce the reported trajectory exactly. There is no other identified error in the method or results.
I[n+1] = I[n] + T e[n]
Choose a verdict and the main rationale.
Notes: 24 fictional manuscript cards for Revise & Reject. Eight cards each are intended Accept, Revise, and Reject. Eight cards each are Guided, Standard, and Advanced. Slides alternate front and answer back. All visible content, including equations, is editable text. Duplicate a front/back pair to add a card. Keep the manuscript ID identical on both sides. Change the expertise tag or fictional author names to match your reviewer profiles. All scenarios, authors, and trial data are fictional. The intended verdict addresses the explicitly stated claim and contribution at the card level, not a complete real-world journal assessment. The PDF uses two 7 × 5 inch cards per US Letter page, with alternating front/back pages. Print at actual size, double-sided, flip on long edge. Test one sheet before a full run. Shuffle complete front/back cards before play.
Manuscript M18. Intended outcome: Revise. Accepted rationale(s): Clarity/Reproducibility.
This example uses a fictional scenario and a direct check of the information on the card.

## Slide 36
REVISE & REJECT
M18 / ANSWER
The Missing Clock
REVISE
ACCEPTED RATIONALE
Clarity/Reproducibility
T changes the numerical controller and the physical timing of the simulation. The supplied information therefore does not specify a unique experiment. A missing implementation parameter can be supplied without replacing the controller study.
REPAIR
State the sample period with units, include it in the code, and confirm that it reproduces the reported trajectory.
Discuss: Would stating only the integral gain remove the ambiguity?
Notes: 24 fictional manuscript cards for Revise & Reject. Eight cards each are intended Accept, Revise, and Reject. Eight cards each are Guided, Standard, and Advanced. Slides alternate front and answer back. All visible content, including equations, is editable text. Duplicate a front/back pair to add a card. Keep the manuscript ID identical on both sides. Change the expertise tag or fictional author names to match your reviewer profiles. All scenarios, authors, and trial data are fictional. The intended verdict addresses the explicitly stated claim and contribution at the card level, not a complete real-world journal assessment. The PDF uses two 7 × 5 inch cards per US Letter page, with alternating front/back pages. Print at actual size, double-sided, flip on long edge. Test one sheet before a full run. Shuffle complete front/back cards before play.
M18 answer. T changes the numerical controller and the physical timing of the simulation. The supplied information therefore does not specify a unique experiment. A missing implementation parameter can be supplied without replacing the controller study.
Repair: State the sample period with units, include it in the code, and confirm that it reproduces the reported trajectory.

## Slide 37
REVISE & REJECT
M19 / ADVANCED
A New Integral Law
Tess Gray, Theo Reed
Primary expertise: Feedback/PID
A research journal requires an original methodological contribution. A cited prior controller uses error e and integral state z with u = 2e + 0.5z and dz/dt = e. The proposed controller only renames z as q. All equations, assumptions, and gains remain identical. The paper offers no new analysis or other result. Its entire contribution is the claimed new controller law.
Prior: u = 2e + 0.5z Proposed: u = 2e + 0.5q
Choose a verdict and the main rationale.
Notes: 24 fictional manuscript cards for Revise & Reject. Eight cards each are intended Accept, Revise, and Reject. Eight cards each are Guided, Standard, and Advanced. Slides alternate front and answer back. All visible content, including equations, is editable text. Duplicate a front/back pair to add a card. Keep the manuscript ID identical on both sides. Change the expertise tag or fictional author names to match your reviewer profiles. All scenarios, authors, and trial data are fictional. The intended verdict addresses the explicitly stated claim and contribution at the card level, not a complete real-world journal assessment. The PDF uses two 7 × 5 inch cards per US Letter page, with alternating front/back pages. Print at actual size, double-sided, flip on long edge. Test one sheet before a full run. Shuffle complete front/back cards before play.
Manuscript M19. Intended outcome: Reject. Accepted rationale(s): Scope/Novelty.
This example uses a fictional scenario and a direct check of the information on the card.

## Slide 38
REVISE & REJECT
M19 / ANSWER
A New Integral Law
REJECT
ACCEPTED RATIONALE
Scope/Novelty
Renaming the integral state leaves the controller unchanged. Under the explicit journal requirement, the paper has no original methodological contribution. The issue is not that the controller must be technically incorrect.
FUNDAMENTAL FLAW
Meeting the venue's requirement would require a substantive new contribution. Correcting the novelty sentence alone would leave no contribution of the required kind.
Discuss: Could this same controller appear appropriately in a teaching paper?
Notes: 24 fictional manuscript cards for Revise & Reject. Eight cards each are intended Accept, Revise, and Reject. Eight cards each are Guided, Standard, and Advanced. Slides alternate front and answer back. All visible content, including equations, is editable text. Duplicate a front/back pair to add a card. Keep the manuscript ID identical on both sides. Change the expertise tag or fictional author names to match your reviewer profiles. All scenarios, authors, and trial data are fictional. The intended verdict addresses the explicitly stated claim and contribution at the card level, not a complete real-world journal assessment. The PDF uses two 7 × 5 inch cards per US Letter page, with alternating front/back pages. Print at actual size, double-sided, flip on long edge. Test one sheet before a full run. Shuffle complete front/back cards before play.
M19 answer. Renaming the integral state leaves the controller unchanged. Under the explicit journal requirement, the paper has no original methodological contribution. The issue is not that the controller must be technically incorrect.
Fundamental flaw: Meeting the venue's requirement would require a substantive new contribution. Correcting the novelty sentence alone would leave no contribution of the required kind.

## Slide 39
REVISE & REJECT
M20 / STANDARD
An Old Tool, A New Study
Hugo Moss, Tess Gray
Primary expertise: Feedback/PID
A journal accepts original experimental control studies. A paper cites the standard PI law and contributes a new, fully documented comparison of two anti-windup settings on a pump. Its measurements support the stated recovery comparison. The abstract nevertheless claims that the paper introduces the first PI controller. The experimental contribution does not depend on inventing that law.
Contribution: new pump tests using an existing PI law
Choose a verdict and the main rationale.
Notes: 24 fictional manuscript cards for Revise & Reject. Eight cards each are intended Accept, Revise, and Reject. Eight cards each are Guided, Standard, and Advanced. Slides alternate front and answer back. All visible content, including equations, is editable text. Duplicate a front/back pair to add a card. Keep the manuscript ID identical on both sides. Change the expertise tag or fictional author names to match your reviewer profiles. All scenarios, authors, and trial data are fictional. The intended verdict addresses the explicitly stated claim and contribution at the card level, not a complete real-world journal assessment. The PDF uses two 7 × 5 inch cards per US Letter page, with alternating front/back pages. Print at actual size, double-sided, flip on long edge. Test one sheet before a full run. Shuffle complete front/back cards before play.
Manuscript M20. Intended outcome: Revise. Accepted rationale(s): Scope/Novelty.
This example uses a fictional scenario and a direct check of the information on the card.

## Slide 40
REVISE & REJECT
M20 / ANSWER
An Old Tool, A New Study
REVISE
ACCEPTED RATIONALE
Scope/Novelty
The abstract overstates the novelty of the controller despite the cited prior law. The experimental study is a separate contribution that fits the stated venue. Correcting the attribution and novelty claim preserves that study.
REPAIR
Describe the PI law as existing work and state the new contribution as the pump experiment and its supported comparison.
Discuss: Which part of this paper can remain original after the correction?
Notes: 24 fictional manuscript cards for Revise & Reject. Eight cards each are intended Accept, Revise, and Reject. Eight cards each are Guided, Standard, and Advanced. Slides alternate front and answer back. All visible content, including equations, is editable text. Duplicate a front/back pair to add a card. Keep the manuscript ID identical on both sides. Change the expertise tag or fictional author names to match your reviewer profiles. All scenarios, authors, and trial data are fictional. The intended verdict addresses the explicitly stated claim and contribution at the card level, not a complete real-world journal assessment. The PDF uses two 7 × 5 inch cards per US Letter page, with alternating front/back pages. Print at actual size, double-sided, flip on long edge. Test one sheet before a full run. Shuffle complete front/back cards before play.
M20 answer. The abstract overstates the novelty of the controller despite the cited prior law. The experimental study is a separate contribution that fits the stated venue. Correcting the attribution and novelty claim preserves that study.
Repair: Describe the PI law as existing work and state the new contribution as the pump experiment and its supported comparison.

## Slide 41
REVISE & REJECT
M21 / GUIDED
A Classroom Control Study
Zoe King, Ari Dunn
Primary expertise: Feedback/PID
An education journal accepts activities using established control methods. A paper compares proportional and PI control on a specified simulated plant. It cites the laws and provides complete code, parameters, and expected outputs. Its contribution is this classroom activity. It claims no new theorem or measured improvement in student learning.
Venue scope: reproducible control-teaching activities
Choose a verdict and the main rationale.
Notes: 24 fictional manuscript cards for Revise & Reject. Eight cards each are intended Accept, Revise, and Reject. Eight cards each are Guided, Standard, and Advanced. Slides alternate front and answer back. All visible content, including equations, is editable text. Duplicate a front/back pair to add a card. Keep the manuscript ID identical on both sides. Change the expertise tag or fictional author names to match your reviewer profiles. All scenarios, authors, and trial data are fictional. The intended verdict addresses the explicitly stated claim and contribution at the card level, not a complete real-world journal assessment. The PDF uses two 7 × 5 inch cards per US Letter page, with alternating front/back pages. Print at actual size, double-sided, flip on long edge. Test one sheet before a full run. Shuffle complete front/back cards before play.
Manuscript M21. Intended outcome: Accept. Accepted rationale(s): Scope/Novelty, Clarity/Reproducibility.
This example uses a fictional scenario and a direct check of the information on the card.

## Slide 42
REVISE & REJECT
M21 / ANSWER
A Classroom Control Study
ACCEPT
ACCEPTED RATIONALE
Scope/Novelty / Clarity/Reproducibility
The stated contribution matches the venue's explicit scope. Using established controllers is appropriate for this teaching activity, and the supplied materials support reproduction. The paper accurately limits what it contributes.
BASIS FOR ACCEPTANCE
A new theorem is unnecessary for the stated submission type. The activity and materials are the contribution the venue requests.
Discuss: Would a journal requiring a new control method assess its scope differently?
Notes: 24 fictional manuscript cards for Revise & Reject. Eight cards each are intended Accept, Revise, and Reject. Eight cards each are Guided, Standard, and Advanced. Slides alternate front and answer back. All visible content, including equations, is editable text. Duplicate a front/back pair to add a card. Keep the manuscript ID identical on both sides. Change the expertise tag or fictional author names to match your reviewer profiles. All scenarios, authors, and trial data are fictional. The intended verdict addresses the explicitly stated claim and contribution at the card level, not a complete real-world journal assessment. The PDF uses two 7 × 5 inch cards per US Letter page, with alternating front/back pages. Print at actual size, double-sided, flip on long edge. Test one sheet before a full run. Shuffle complete front/back cards before play.
M21 answer. The stated contribution matches the venue's explicit scope. Using established controllers is appropriate for this teaching activity, and the supplied materials support reproduction. The paper accurately limits what it contributes.
Basis for acceptance: A new theorem is unnecessary for the stated submission type. The activity and materials are the contribution the venue requests.

## Slide 43
REVISE & REJECT
M22 / ADVANCED
Beyond the Linearization
Theo Reed, Nia Volt
Primary expertise: Stability
For the nonlinear continuous-time system below, the authors correctly compute the linearization at the origin as dx/dt = −x. They conclude that every initial state converges to zero. This global asymptotic-stability claim is the paper's sole result. The paper places no restriction on x(0) and explicitly includes x(0) = 2 among the claimed cases.
dx/dt = −x + x³
Choose a verdict and the main rationale.
Notes: 24 fictional manuscript cards for Revise & Reject. Eight cards each are intended Accept, Revise, and Reject. Eight cards each are Guided, Standard, and Advanced. Slides alternate front and answer back. All visible content, including equations, is editable text. Duplicate a front/back pair to add a card. Keep the manuscript ID identical on both sides. Change the expertise tag or fictional author names to match your reviewer profiles. All scenarios, authors, and trial data are fictional. The intended verdict addresses the explicitly stated claim and contribution at the card level, not a complete real-world journal assessment. The PDF uses two 7 × 5 inch cards per US Letter page, with alternating front/back pages. Print at actual size, double-sided, flip on long edge. Test one sheet before a full run. Shuffle complete front/back cards before play.
Manuscript M22. Intended outcome: Reject. Accepted rationale(s): Math/Logic, Stability/Performance.
Background references for the technical principle:
https://underactuated.mit.edu/acrobot.html

## Slide 44
REVISE & REJECT
M22 / ANSWER
Beyond the Linearization
REJECT
ACCEPTED RATIONALE
Math/Logic / Stability/Performance
The stable linearization supports local behavior near zero, not this global claim. For x > 1, x³ − x > 0, so the trajectory starting at 2 moves away from zero. Also, x = 1 and x = −1 are nonzero equilibria.
FUNDAMENTAL FLAW
Replacing the sole global result with a local result materially changes the contribution. The original universal claim is directly false.
Discuss: What interval of initial states actually converges to zero?
Notes: 24 fictional manuscript cards for Revise & Reject. Eight cards each are intended Accept, Revise, and Reject. Eight cards each are Guided, Standard, and Advanced. Slides alternate front and answer back. All visible content, including equations, is editable text. Duplicate a front/back pair to add a card. Keep the manuscript ID identical on both sides. Change the expertise tag or fictional author names to match your reviewer profiles. All scenarios, authors, and trial data are fictional. The intended verdict addresses the explicitly stated claim and contribution at the card level, not a complete real-world journal assessment. The PDF uses two 7 × 5 inch cards per US Letter page, with alternating front/back pages. Print at actual size, double-sided, flip on long edge. Test one sheet before a full run. Shuffle complete front/back cards before play.
M22 answer. The stable linearization supports local behavior near zero, not this global claim. For x > 1, x³ − x > 0, so the trajectory starting at 2 moves away from zero. Also, x = 1 and x = −1 are nonzero equilibria.
Fundamental flaw: Replacing the sole global result with a local result materially changes the contribution. The original universal claim is directly false.
Background references:
https://underactuated.mit.edu/acrobot.html

## Slide 45
REVISE & REJECT
M23 / ADVANCED
Stability Under Scheduling
Mira Chen, Tess Gray
Primary expertise: Stability
A study models dx/dt = −a(t)x, with piecewise-continuous a(t) in [0.5, 2]. It claims uniform exponential decay and compares scheduled decay trajectories. Its proof gives x(t) = exp(−at)x(0) for constant a, then uses this expression for varying a(t). The trajectory study itself allows varying schedules. The model and bounds above are explicit.
dx/dt = −a(t)x, 0.5 ≤ a(t) ≤ 2
Choose a verdict and the main rationale.
Notes: 24 fictional manuscript cards for Revise & Reject. Eight cards each are intended Accept, Revise, and Reject. Eight cards each are Guided, Standard, and Advanced. Slides alternate front and answer back. All visible content, including equations, is editable text. Duplicate a front/back pair to add a card. Keep the manuscript ID identical on both sides. Change the expertise tag or fictional author names to match your reviewer profiles. All scenarios, authors, and trial data are fictional. The intended verdict addresses the explicitly stated claim and contribution at the card level, not a complete real-world journal assessment. The PDF uses two 7 × 5 inch cards per US Letter page, with alternating front/back pages. Print at actual size, double-sided, flip on long edge. Test one sheet before a full run. Shuffle complete front/back cards before play.
Manuscript M23. Intended outcome: Revise. Accepted rationale(s): Math/Logic, Model/Assumptions.
This example uses a fictional scenario and a direct check of the information on the card.

## Slide 46
REVISE & REJECT
M23 / ANSWER
Stability Under Scheduling
REVISE
ACCEPTED RATIONALE
Math/Logic / Model/Assumptions
The displayed constant-coefficient solution is not the solution for a general schedule. However, the claimed bound is repairable: x(t) = exp(−∫₀ᵗ a(s)ds)x(0), so |x(t)| ≤ exp(−0.5t)|x(0)|. The stated assumptions already suffice.
REPAIR
Replace the constant-a argument with the integral solution or a uniform Lyapunov bound. The decay claim and scheduling study can remain.
Discuss: Why is the lower bound on a(t) useful for a uniform decay rate?
Notes: 24 fictional manuscript cards for Revise & Reject. Eight cards each are intended Accept, Revise, and Reject. Eight cards each are Guided, Standard, and Advanced. Slides alternate front and answer back. All visible content, including equations, is editable text. Duplicate a front/back pair to add a card. Keep the manuscript ID identical on both sides. Change the expertise tag or fictional author names to match your reviewer profiles. All scenarios, authors, and trial data are fictional. The intended verdict addresses the explicitly stated claim and contribution at the card level, not a complete real-world journal assessment. The PDF uses two 7 × 5 inch cards per US Letter page, with alternating front/back pages. Print at actual size, double-sided, flip on long edge. Test one sheet before a full run. Shuffle complete front/back cards before play.
M23 answer. The displayed constant-coefficient solution is not the solution for a general schedule. However, the claimed bound is repairable: x(t) = exp(−∫₀ᵗ a(s)ds)x(0), so |x(t)| ≤ exp(−0.5t)|x(0)|. The stated assumptions already suffice.
Repair: Replace the constant-a argument with the integral solution or a uniform Lyapunov bound. The decay claim and scheduling study can remain.

## Slide 47
REVISE & REJECT
M24 / ADVANCED
The Cost of Correction
Ari Dunn, Mira Chen
Primary expertise: Optimal Control
The authors solve an unconstrained continuous-time LQR problem for dx/dt = −x + u with cost J = ∫₀∞(x² + u²)dt. They use P = √2 − 1 and u = −Px. Their derivation checks P² + 2P − 1 = 0 and obtains the stable closed-loop pole −√2. They claim this feedback minimizes the stated cost and gives J = Px(0)². The model has no noise or input bounds.
P = √2 − 1 u = −Px J = ∫₀∞(x² + u²)dt
Choose a verdict and the main rationale.
Notes: 24 fictional manuscript cards for Revise & Reject. Eight cards each are intended Accept, Revise, and Reject. Eight cards each are Guided, Standard, and Advanced. Slides alternate front and answer back. All visible content, including equations, is editable text. Duplicate a front/back pair to add a card. Keep the manuscript ID identical on both sides. Change the expertise tag or fictional author names to match your reviewer profiles. All scenarios, authors, and trial data are fictional. The intended verdict addresses the explicitly stated claim and contribution at the card level, not a complete real-world journal assessment. The PDF uses two 7 × 5 inch cards per US Letter page, with alternating front/back pages. Print at actual size, double-sided, flip on long edge. Test one sheet before a full run. Shuffle complete front/back cards before play.
Manuscript M24. Intended outcome: Accept. Accepted rationale(s): Math/Logic, Stability/Performance.
Background references for the technical principle:
https://underactuated.mit.edu/lqr.html

## Slide 48
REVISE & REJECT
M24 / ANSWER
The Cost of Correction
ACCEPT
ACCEPTED RATIONALE
Math/Logic / Stability/Performance
The scalar Riccati equation is 1 − 2P − P² = 0. Its positive stabilizing solution is √2 − 1, giving the pole −1 − P = −√2. The standard LQR result gives the optimal value Px(0)² for the stated unconstrained problem.
BASIS FOR ACCEPTANCE
The gain, Riccati check, closed-loop stability, and cost claim agree under the supplied assumptions.
Discuss: What would need reassessment if the actuator imposed |u| ≤ 1?
Notes: 24 fictional manuscript cards for Revise & Reject. Eight cards each are intended Accept, Revise, and Reject. Eight cards each are Guided, Standard, and Advanced. Slides alternate front and answer back. All visible content, including equations, is editable text. Duplicate a front/back pair to add a card. Keep the manuscript ID identical on both sides. Change the expertise tag or fictional author names to match your reviewer profiles. All scenarios, authors, and trial data are fictional. The intended verdict addresses the explicitly stated claim and contribution at the card level, not a complete real-world journal assessment. The PDF uses two 7 × 5 inch cards per US Letter page, with alternating front/back pages. Print at actual size, double-sided, flip on long edge. Test one sheet before a full run. Shuffle complete front/back cards before play.
M24 answer. The scalar Riccati equation is 1 − 2P − P² = 0. Its positive stabilizing solution is √2 − 1, giving the pole −1 − P = −√2. The standard LQR result gives the optimal value Px(0)² for the stated unconstrained problem.
Basis for acceptance: The gain, Riccati check, closed-loop stability, and cost claim agree under the supplied assumptions.
Background references:
https://underactuated.mit.edu/lqr.html